## Slide 1: A case for accelerator based VR content generation on edge towards energy-efficiency
Presented by: Sridhar Gunnam
Advisor: Prof. Robert LiKamWa

## Slide 2: Proliferation of VR in different applications
Remote Robotic Vision
VR tour to Mars
Notes: We can imagine looking into VR headset and performing tasks remotely.
Robot is mixing the chemicals
Person is inspecting mars remotely.

## Slide 3: Proliferation of VR in different applications
Watching a soccer match in VR
Notes: Enjoying a soccer match as if you were there in the stadium.
Enjoying such experience means immersion in the scene.

## Slide 4: VR needs highly immersive experience
3D(depth)
Notes:   The ability to look around and to perceive how far or how near things are away from you?
  Is 360 and 3D enough?

## Slide 5: VR needs higher resolution
VR needs >16k Resolution.
4k for VR is like 144p for mobile
Pixelated view
Notes:   Each degree in VR needs 60 pixels. 4k  10 pixels/degree
  How do we generate how resolution and immersive content for VR?

## Slide 6: Content generation for VR is an emerging research problem
Untethered and long battery life
Low latency
High data rates and high computations
But low power and low latency??
Notes: Because of high resolution we have higher data rates!
But we need low power for battery constrained capture device,
Low latency for realtime applications

## Slide 7: What does low power and low latency mean?
Power of device is in the range of few Watts.
Capture and compute is in few hundreds of milliseconds.
Notes: Can commertial solutons solve this problem?provide this?

## Slide 8: Commercial solutions consume high power
High compute power
  1000’s of CPU’s
  Or Several GPU’s
If 10% of US population uses VR at a given time
  #GPU’s needed = 32.5 Million
  Power burnt = 27625 Mega Watts
~1-2 Hours
Capture Time
Notes: Capture and offload !
http://360rumors.com/2018/05/best-worlds-insta360-pro-hands-real-world-review-part-1-sample-photos-videos.html#guide

## Slide 9: 27625 Mega Watts: Greater than world’s largest power plant “ The Three Gorges”
Notes: What are going to do?
Build another dam for AR and MR

## Slide 10: In terms of Hoover Dams!!
15 of those

## Slide 11: Commercial solutions are have very high latency
High compute latency
  1 hour of video takes 10 hours to stitch.
Network Latency
  Sending the camera frames will be twice as expensive as sending the output panorama
  Compression and decompression stages will dominate end-to-end latency.
Notes: http://360rumors.com/2018/05/best-worlds-insta360-pro-hands-real-world-review-part-1-sample-photos-videos.html#guide

## Slide 12: Can we come up with a viable solution?
That is
Low Power
Low Latency
Edge processing
Notes: Edge means computing near the device used for capture. Reduce end-to-end latency
Which is the best way to analize the challenges and come up with viable solution
Why we need a hardware sys?

## Slide 13: Remainder of the talk
Building a prototype
Characterization
Proposed optimizations
Notes: Which is the best way to analize the challenges and come up with viable solution

## Slide 14: Remainder of the talk
Building a prototype
Characterization
Proposed optimizations

## Slide 15: System Overview: Camera + Processor + Storage
ISP
CPU
Camera
DRAM
DDR
CSI
Frontend
Backend
Capture
Processing
Notes: The system consists of different pieces of hardware.
Interface glues these systems.

## Slide 16: Camera system: How many cameras do we need?
Depends on field of view of camera lens
  We use wide field of view lens
  and 6 cameras
Minimum distance b/w scene objects and camera
Size of camera
Typ. Mobile Cameras
60º FOV
Fisheye Cameras
140º FOV to 210º FOV

## Slide 17: Processing Sub-System: CPU/GPU
In our system:
  Quad core ARM A57
  8 GB DRAM

## Slide 18: Interfaces in the System: CSI and DDR
Jetson Camera Interface

## Slide 19: Prototype
Hardware:
  Six Sony IMX 274 Cameras, wide fisheye lens
  Nvidia Jetson TX2
    ARM A57 quad core processor
    Dual ISP with 1200 Million pixels/sec
Software:
  Ubuntu 16.04 LTS
  c++, openCV
  Facebook surround 360
IMX274 cameras
CSI Interface
Jetson TX2
Disk
Notes: Putting everything together. Show pride.

## Slide 20: Inputs and outputs of the system
Left Eye
Right Eye
Notes: capture entire 360 x 180, Mono – Portable, usable because of small size. ODS – Depth

## Slide 21: Remainder of the talk
Building a prototype
Characterization
Proposed optimizations

## Slide 22: Key findings
High power consumption
  Redundant capture
  High data rates across interfaces
  Redundant computations
  Huge memory footprint
High processing latency
  Sequential execution
Frontend
Backend
Notes: What does redundant capture?

## Slide 23: (1a) Redundant Capture
~500 mW per camera
Cameras process frames even when the scene is not changing.
Notes: Cameras are dumb.
Natuarally there is lot of redundancy from one image to another
limit scalability of capturing to higher resolution and framerate and multiple of these cameras.

## Slide 24: (1b) Underutilized Capture Pipeline can cost energy efficiency per pixel
Total Energy = Static + Dynamic
Underutilized Resources can cost static energy.

## Slide 25: (2) High interface data rates are expensive
34% of total power
Notes: The interfaces consume major chunk of power during capture.
DRAM is from micron and DRAM power simulator. Camera pulled from data sheet.

## Slide 26: (3) Redundant computations
The computation is done on all the pixels of all the frames.
No reuse of previous results.
~100’s of million operations per output frame
Notes: The frames to frame differences are small, implies that Same like cameras, traditional algorithms are not adaptive to compute only on the changes over the image.

## Slide 27: (4) Under-optimized data abstractions across subsystems increases memory footprint
388MB of data used for optical flow step.
Data format is single precision.
Notes: Work on the figure.

## Slide 28: Key findings
High power consumption
  Redundant capture
  High data rates across interfaces
    4K @ 60 fps
  Underutilized capture pipeline
  Redundant computations
  Huge memory footprint (240 MB)
High processing latency
  Sequential execution
Frontend
Backend

## Slide 29: (1) Sequential execution of computation across frames
Stages | Sequential Execution Time
Projection | 2.89
Optical Flow | 16.21
View Synthesis | 4.5
CPU implementation will take 24 sec to generate each output frame

## Slide 30: Remainder of the talk
Building a prototype
Characterization
Proposed optimizations

## Slide 31: Proposed optimizations
Low power
  Reducing power of sensor
  Spatial-temporal data reuse to minimize redundant computations
Low latency
  Pipelined execution
  Parallelize execution
Frontend
Backend

## Slide 32: (1a) Reducing redundant ADC conversions
Temporal frames are similar!!
Cut down on Analog to Digital conversions
t=0
..
t=3
t=2
t=1
..
Notes: How can we make the cameras smart?
: ADC inside camera burns 60% of the power
Power per pixel is 10 nWatts
ADC Conversion few nanoWatts

## Slide 33: (1a) Reducing redundant ADC Conversions
101101
101110
101111
…
We usually see bit changes only in the lower order bits.
Corresponding bits in previous frame bits can be used to guess higher order bits.

## Slide 34: (1a) Reducing redundant ADC Conversions
ADC
Notes: Binary search and find result in several iterations.
Reduce upto 80% of the total power.
Caution.

## Slide 35: (1b) Near-sensor compression reduces CSI interface power
ISP
CPU
Camera
DRAM
DDR
CSI
4.17 Gbps 1.4 Watts
to
~1.25 Gbps 0.4 Watt
Region based histogram in ISP can be used for encoding sensor data
Notes: Motion vectors from compression can be used to optimize optical flow

## Slide 36: (1b) Near-sensor compression increases the scalability to higher resolution and framerate
Compression can reduces 70% of communication traffic from sensor to Processing unit

## Slide 37: (2) (a) Improving data abstractions across subsystems reduces data requirement.
Problem:
Optical Flow stage loads current and previous frames
Time=t, t-1
Time=t-1
Uses previous frame for motion detection
Time=t, t-1
Notes: Think Globally, Act Locally.

## Slide 38: (2) (b) Under optimized data flow leads to increased memory footprint
Reusing motion vectors from ISP stage, and reusing optical flow buffer reduces data size from 388 MB to 157 MB
Time=t
Time=t
Think Globally, Act Locally.

## Slide 39: Proposed optimizations
Low power
  Reducing power of sensor
  Spatial-temporal data reuse to minimize redundant computations
Low latency
  Pipelined execution
  Parallelize execution
Frontend
Backend

## Slide 40: (1) Pipelined execution of independent pyramids of optical flow reduce latency
Dense optical flow uses 70 % of total computation time

## Slide 41: (1) Pipelined execution of independent pyramids of optical flow reduce latency
~0.5 sec to ~0.1 second

## Slide 42: (2) Parallelize execution
Impl. | CPU Runtime (Normal) | FPGA Impl. Approx.
Projection | 2.89 s | ~3 ms
Optical Flow | 16.21 s | 17 ms
View Synthesis | 4.5 s | ~4.5 ms
0.1 sec to 17 ms
Notes: Highly parallel FPGA architectures can make real-time stitching of 360 video possible
To conclude everything together

## Slide 43: Reduce and reuse data to save power and improve latency.
Optimize Capture Power
  Sensor ADC
Optimize Compute Power
  Data Reuse
  Data flow optimization
Latency
  Pipelining
  Parallelize
Notes: Principles for End-to-End System Optimization

## Slide 44: Summary
VR content generation is an important research problem
Our characterization highlight the bottlenecks in sensor, interface, and processing.
Closer integration of subsystems can help reduce and reuse data.
Proposed solutions make a case for accelerator on edge.

## Slide 45: Extra slides
ODS capture generation

## Slide 46: Background: Stereo Vision

## Slide 47: Background: Binocular Vision and Viewing Circle
Binocular Vision/Stereo Vision needs two views

## Slide 48: Background: How ODS works?
Notes: Extrapolate the rays, if lucky you will find a camera view. Otherwise you can approximate the camera view.

## Slide 49: Background: How ODS works? Optical Flow
Based on depth of each pixel
Synthesize intermediate views

## Slide 50: View Synthesis
MegaStereo, CVPR 2013

## Slide 51: Background: How ODS works? View Synthesis
Instead of synthesizing all the viewpoints, we approximate the rays, thereby saving computations

## Slide 52: That is how we generate ODS Panoramas
Left Eye
Right Eye
Notes: capture entire 360 x 180, Mono – Portable, usable because of small size. ODS – Depth

## Slide 53: Step1– Equirectangular Projection
Multiple cameras streams

## Slide 54: Step2– Overlapping regions b/w adjacent camera views

## Slide 55: Step3– Optical Flow b/w adjacent Cameras

## Slide 56: Step4– Optical Flow (With Temporal Regularization)

## Slide 57: That is how we generate ODS Panoramas
Left Eye
Right Eye
Notes: capture entire 360 x 180, Mono – Portable, usable because of small size. ODS – Depth

## Slide 58: Previous Works
Google Jump. [Halide pipelines, CPU scheduling]
Facebook [multi-threading on CPU]
Muzamder[Halide, parallel GPU]
Our focus:
  To find out inefficiencies in computation.
  To characterize the bottlenecks and propose directions.

## Slide 59: Camera Calibration
Intrinsic
Extrinsic
Rig calibration
Fisheye Circle
  Hough transform of well-lit captures
Fisheye distortion

## Slide 60: System Overview